## Slide 1: Chapter 5 Observing the Atmosphere
ATMO 1300
Summer II 2017

## Slide 2: Chapter 5 Observing the Atmosphere
ATMO 1300
Summer II 2017
Measurement Types
Satellites
Radars

## Slide 3: A couple notes on hail formation
http://www.thedenverchannel.com/weather/viewers-june-storm-photos

## Slide 4
http://www.noaa.gov/features/02_monitoring/images/hail2.jpg

## Slide 5: Two Types of Measurements
Direct Methods
  Taken in place, instruments in direct contact with atmospheric property you are trying to measure
Indirect Methods
  Atmospheric properties measured from a distance (i.e., no direct contact).
  Also referred to as remote sensing.

## Slide 6: Direct Measurements
Automated Surface Observing System (ASOS) – Typically located at airports

## Slide 7: Automated Surface Observing System(ASOS)
Over 600 ASOS sites across North America
Measures and reports standard atmospheric variables with a frequency of 1-60 minutes
  Temperature
  Dew point temperature
  Pressure
  Wind direction/speed
  Rainfall
  Cloud height
  Visibility

## Slide 8: Displaying Surface Observations
Fig. 1-18, p. 25

## Slide 9: Station Model
Fig. 1-17, p. 23

## Slide 10
Wind Direction
We describe the wind direction as where the wind is coming from.
For example, a north wind blows from the North, or 0°
The degrees increase from north to east.
So if the wind direction is 270°, what cardinal direction is that?

## Slide 11: West Texas Mesonet
www.mesonet.ttu.edu

## Slide 12: Meteogram
Box 5-1, p. 128
Displays a time series of meteorological variables for a single station

## Slide 13: How are atmospheric variables measured?
Unique instrumentation exists for each variable

## Slide 14: Temperature
ASOS uses resistance thermometers, which measure the change in electrical resistance of a piece of metal (a function of temperature)
Often sheltered by a white “Stevenson Screen”, protecting thermometer from direct solar irradiation
Well ventilated
Fig. 5-2, p. 146

## Slide 15: Humidity
Hygrometers – An instrument that measures humidity
ASOS: Capacitance (cheap, accurate, easy) – the ability of an object to store charge varies with relative humidity
Psychrometer – finds the temperature something can be cooled to due to evaporation (depends on temperature and moisture content, known as the wet bulb temperature) which can be compared to temperature to find humidity values
GPS – measure the delay of a radio wave (which travels slower through water vapor)

## Slide 16: Humidity
Dew point hygrometer
Also called a “chilled mirror sensor”
A clean mirror will exactly reflect laser light to the receiver
Temperature of mirror is decreased incrementally until water vapor condenses on it. Laser light scattered by the water droplets, reduction in intensity at receiver, dewpoint temperature reported.
2nd Edition: Fig. 5-3, p. 130

## Slide 17: Pressure
Mercury barometers (top) and aneroid barometers (bottom) are what we are used to.
ASOS uses electronic barometers.
Fig. 5-3, p. 147

## Slide 18: Wind Direction / Speed
Cup anemometer used to measure wind speed
Wind vane used to measure wind direction
Also, there are sonic anemometers (below), which measure how wind affects the propagation of acoustic energy (no moving parts!)

## Slide 19: Precipitation
Tipping bucket rain gauge
Upper heated collector (melts frozen precipitation)
Collector empties into bucket underneath, which tips and empties after every 0.01” of precipitation is collected.
Wind guard around outside to keep precipitation from blowing across opening.

## Slide 20: Snow accumulation
Not automated!
Carefully hand measured
Generally 12 in of snow = 1 in of rain when melted, but this number varies greatly!
Source: www.stamfordadvocate.com

## Slide 21: Measuring the Upper Atmosphere
Upper atmosphere is sorely undersampled
These measurements needed for improved model forecasts!
Radiosondes released twice a day from stations spaced far apart

## Slide 22: Radiosondes

## Slide 23: Radiosondes – and more!

## Slide 24: Indirect Measurements
Two forms:
  Active sensors – transmit and receive energy
  Passive sensors – just receive energy
Examples?

## Slide 25: Satellite Observations
Two orbits for satellites
  Geosynchronous or Geostationary orbit – 36,000 km above Earth’s surface.
    Satellite rotates at same rate that the planet does. Therefore, the satellite constantly views the same footprint on Earth.
    Good for constructing animations to determine motion of atmospheric features .
  Low earth orbit (~ 500 miles above the surface)
    Satellite rotates faster than the planet
    Therefore, this strategy is good for scanning many portions of the planet
    Usually, scans are from pole to pole

## Slide 26
Fig. 5-13, p. 157

## Slide 27: Typical coverage for a low-earth orbit
http://sharaku.eorc.jaxa.jp/AMSR/ocean_wind/manual/images/sunglitter_e.bmp

## Slide 28: Operational U. S. Satellites
Geostationary Operational Environmental Satellite (GOES)

## Slide 29: Types of Satellite Imagery
Visible
  What we have seen thus far
  Solar radiation reflected/scattered by earth and atmosphere
Infrared
  Allows us to visualized how much infrared energy the earth and atmosphere are emitting
  Tells us the temperature of the emitting substance
  For clouds, this information is valuable for determining altitude of cloud tops!

## Slide 30: Visible Satellite Animations
http://weather.cod.edu/satrad/
http://weather.cod.edu/satrad/exper/?parms=northcentral-02-24-1

## Slide 31: Recall Wien’s Law
λmax = C / T
The wavelength of maximum emission is inversely proportional to temperature
Graphic from www.cira.colostate.edu/ramm/goes39
Fig. 2-8, p. 36

## Slide 32: Visible vs. Infrared
VISIBLE satellite image
INFRARED satellite image
X
X
X
X
cold
warm

## Slide 33: Types of Satellite Imagery
Water Vapor
  Tracks infrared emission primarily from water vapor (6.5-7 mm)
  Altitude of emission: 300-600 mb
  Can track upper-atmospheric flow
  Useful for diagnosing upper-air weather pattern (e.g., troughs, ridges…more later)
  Since water vapor exists in some proportion everywhere across the globe, continuous surveillance of flow is possible (do not need to have clouds)

## Slide 34: Sensing Lightning
Lightning is very hot (3x hotter than the surface of the sun) -> emits a large amount of radiation
Ground strike data – passive sensors using a wide range of wavelengths such as NLDN (National Lightning Detection Network): http://www.lightningstorm.com/explorer.html
In cloud – Lightning Mapping Arrays: passive sensors using wavelengths in radio bands, more dense network of stations

## Slide 35
http://pogo.tosm.ttu.edu/about/

## Slide 36
Photo and analysis courtesy of: Eric Bruning, Pat Skinner

## Slide 37: Radar (Radio Detection and Ranging)

## Slide 38: RADAR basics
Electromagnetic energy transmitted into atmosphere
Backscattered energy (“radar echo”) measured by radar and displayed
The larger the object, the more energy that is returned. Therefore, the intensity of the radar echo tells us how much precipitation is falling
Sources of backscattering: raindrops, hail, snow, bugs, dust, ground targets, debris
Fig. 5-19, p. 162

## Slide 39: Example of Radar Reflectivity
0.5 degree elevation

## Slide 40: Storm Total Precipitation

## Slide 41: WSR-88D Doppler Radar

## Slide 42: Doppler Effect
Johann Christian Doppler (1803-1853)
Apparent frequency of radiation is affected by motion of emitting source
  Frequency increases for motion towards observer
  Frequency decreases for motion away from observer
Can use this effect to deduce motion of scatterers in atmosphere (driven by wind)

## Slide 43: Doppler Effect Animation
Fig. 5-21, p. 164
https://www.youtube.com/watch?v=a3RfULw7aAY

## Slide 44: Radar Technology
The National Weather Service has installed and operates / maintains a network of large scale Doppler radars.
The are for “surveillance” purposes, not necessarily research. So they are designed to see a long way, but with low resolution.
We can see:
  Reflectivity – the raindrops in a storm; gives an idea of storm shape and structure
  Radial velocity – The RADIAL motion of the raindrops.
  Whether the objects are larger in the horizontal or vertical
We can’t see:
  Tornadoes
  The actual wind speed/ dir.
  Close to the ground

## Slide 46: WSR-88D Network

## Slide 47: Research Radars
Doppler on Wheels (DOW) –
Center for Severe Weather Research
Shared Mobile Atmospheric Research
and Teaching Radar (SMART-R) –
Texas Tech, Texas A&M,
University of Oklahoma,
National Severe Storms Laboratory
University of Massachusetts Tornado Radar
Last but not least….

## Slide 48: TTU-Ka Mobile Doppler Radars

## Slide 49
….and recently upgraded – larger dish = higher sensitivity

## Slide 50: Mobility
With a small dish and transmitter, we can put the whole ensemble on the bed of a truck. This allows us to:
  Drive to what ever phenomena we are interested in
  Obtain measurements very close to the surface.

## Slide 51: Differences in resolution

## Slide 52: TTUKa Tornado Radar Data 15 April 2012
Reflectivity
Velocity

## Slide 53: UMass Tornado Radar Data 3 May 1999
Reflectivity
Velocity

## Slide 54: But why 2 radars?
We can use the data from both radars in a dual-Doppler synthesis to retrieve the actual wind speed and direction

## Slide 55: Wind Profilers
Wind direction and speed inferred from three separate radar beams (one vertical, two orthogonal oblique)
Vertical profiling
Image from B. Geerts
Univ. of Wyoming

## Slide 56
Fig. 5-24, p. 167

## Slide 57: Other Methods
SODAR – SOund Detection And Ranging
LIDAR – LIght Detection And Ranging
Often used similar to profilers

## Slide 58: Things to Remember
Direct measurements (in contact) vs Indirect (remote sensing)
ASOS – official surface measurements
Know how to decode a surface observation
Meteogram – pictorial time series of observations from one station
Know which instrument measures which property of the atmosphere
Direct measure of upper
atmosphere: radiosonde

## Slide 59: Passive Indirect Measurements
Satellite
  Geosynchronis – high altitude, always point at the same side of the Earth (ex: GOES)
  Low earth orbit – rotate typically pole to pole and cover the whole globe (ex: TERRA)
  Three commonly used types of imaging
    Visible
    Infrared - temps of clouds
    Water vapor - upper air motions
Lightning systems
  Ground-strike data
  In-cloud mapping

## Slide 60: Active Indirect Measurements
RADAR
Emits EM wave, measures echo of EM wave, larger object = larger return - can be used to estimate total amount of rainfall
Doppler effect – the change of the frequency of the EM wave due to the radial motion of the things scattering the energy – higher frequency by something moving towards the radar
WSR-88D: national network, low resolution, large area covered
  Sees rain, hail, snow, birds, insects, bats, debris, wind turbines and motion of these things to/from the radar (radially)
  Does not see air movement or things close to the ground
Mobile research radars – much higher detail, closer to the surface, mobile, can see much smaller scatterers
Profilers – used to map vertical profiles of wind speeds and directions